## Slide 1
Bojie Li*1,2 Tianyi Cui*3 Zibo Wang1,2 Wei Bai1 Lintao Zhang1
1Microsoft Research 2USTC 3University of Washington
* Co-first authors
SocksDirect: Datacenter Sockets can be Fast and Compatible
Presenter: Bojie Li
Distributed and Parallel Software Lab, Central Software Institute, Huawei 2012 Labs

## Slide 2: The Socket Communication Primitive
socket()
bind()
listen()
accept()
recv()
send()
close()
Server
Client
socket()
connect()
send()
recv()
close()
Notes: As we all know, most applications use the socket primitive for inter-process communication, both within a same server and among different servers.

## Slide 3: Socket: a Performance Bottleneck
Socket syscall time >> user application time
Chart: 
| Lighttpd HTTP Server | Nginx HTTP Load Balancer | Redis Key-Value Store | NSC DNS Server
Kernel time | 0.78 | 0.77 | 0.87 | 0.92
User application time | 0.22 | 0.23 | 0.13 | 0.08
Socket latency >> hardware transport latency
Chart: 
| Intra-host (vs. shared memory) | Inter-host (vs. RDMA)
shared memory (SHM) / RDMA | 0.25 | 1.6
Linux Socket | 11 | 30
Notes: Traditionally, sockets are implemented in the OS kernel. We all know that kernel socket is very slow. To show this point, we profile several popular applications in data centers. We can see that 70% to 90% of CPU time is used in OS kernel, which means it is handling the socket system calls. If we could eliminate the overhead of OS kernel and all CPU time can be utilized by the user space application, the application throughput will improve by several times.
Next we look at the latency, and the problem is more severe than throughput. For communication between two directly connected servers, socket latency is 17x of RDMA. For intra-host communication, socket latency is 40x of shared memory queue. In this work, we try to answer one question: is this socket overhead an intrinsic property of the socket abstraction, or we can do something to eliminate the socket overhead?

## Slide 4: Timeline of the SocksDirect Project
2017/04 | Start research on high-performance socket, IPC and container networking.
2017/07 | IPC-Direct: Fast and Compatible Container Networking won the most impactful award and global 1st place in Cloud & Enterprise category in Microsoft Hackathon 2017.
2017/08 | Submitted a poster to SOSP’17 Student Research Competition, admitted in final presentation rounds.
2018/04 | First submission to OSDI’18 but rejected in first-round review. Major reasons: difference from related work; presentation is not clear.
2018/09 | Second submission to NSDI’19 but rejected in first-round review. Major reasons: design is too complicated; evaluation not solid.
2019/01 | Third submission to SIGCOMM’19 and accepted. Improve discussion on related work; remove unnecessary goals and simplify design; make the prototype work on real applications.

## Slide 5: High Performance Socket Systems
User App
User App
User App
Kernel VFS
Host 1
Host 2
Kernel Optimization
FastSocket, Megapipe, StackMap…
User-space TCP/IP
Offload to RDMA NIC
IX, Arrakis, SandStorm, mTCP, LibVMA, OpenOnload…
Rsocket, SDP, FreeFlow…
User App
User-space VFS
User App
User-space VFS
Host 1
TCP/IP
TCP/IP
User App
Host 2
Kernel TCP/IP
NIC packet API
User-space TCP/IP
User-space TCP/IP
NIC packet API
NIC packet API
Kernel
NIC packet API
User-space Stack
User App
User-space VFS
User App
User-space VFS
Host 1
RDMA
User App
Host 2
NIC RDMA API Hardware-based Transport
NIC RDMA API
User-space VFS
Notes: There have been extensive research to improve the performance of socket systems.
The first category is to optimize the kernel. A socket stack basically divides into three layers. The first layer is the virtual file system, VFS, because each socket connection is regarded as a file in Linux, and a file descriptor is mapped for the socket. The second layer is the kernel TCP/IP stack that provides the transport function. The third layer is the hardware interface layer. Linux kernel uses a packet API.
The second category is to implement the VFS abstraction and TCP/IP transport in the user space. It not only move the kernel functions into user space, but also greatly simplify the functions, for example, use polling to avoid the interrupt and process scheduling overheads.
The third category is to offload the transport to the NIC. Here we recall some history of hardware-based transports. TCP offload is not a new thing. In 1990s, there has been Ethernet cards that

## Slide 6: Takeaways: related work
OSDI’18 Review: On the inter-server socket side, there have already been several proposals in socket over RDMA, including SDP, libvma, rsocket, OpenUCX, and UNH EXS. Among these, SDP, UNH EXS, rsocket all support zero copy (in some of their modes). There are no performance comparison with these solutions or related work discussion of SocksDirect's difference. There are also a bunch of user-level TCP/IP implementation.
OSDI’18 Review: There has been a whole lot of work on high-performance stacks… The related work (and Table 3) would do better to contrast with these in terms of design rather than features… You mention highly similar systems like mTCP, but completely fail to make any characterization about what insights or lessons you've had that are different than theirs. SDP has highly similar goals to yours, and contrary to what you claim in the related work section was designed to be transparent to applications.
OSDI’18 Review: Zero copy or shared memory communication isn’t new. Note that even recent Linux TCP stacks support zero copy.
SIGCOMM’19 PC Meeting Summary: We also feel that you need to relate your work to LITE (Tsai and Zhang, SOSP'17). While LITE does not allow transparent substitution, it has similar goals and techniques to your work.

## Slide 7: Takeaways: related work / motivation
NSDI’19 Review: Another doubt I have is about the need to transparently support socket functionality in this richer set of scenarios. The paper makes the point that previous approaches do not work across fork, or that they do not support intra-machine communication. … But a practical question here is whether this support for full semantics is actually needed. I didn't see the compelling applications that do not work on previous approaches because such support is lacking.
NSDI’19 Review: Similarly, I strongly suspect that another reason that previous work has not focused on intra-machine performance is that the application scenarios haven't demanded it. … can you start the introduction by listing important applications that cannot use previous high-performance networking stacks because they lack support for fork, intra-machine communication, etc.?

## Slide 8: Takeaways: related work / motivation
OSDI’18 Review: I did not understand why we should use a TCP socket for intra-machine communication instead of a unix domain socket or a pipe. The latter performs much better on Linux, but evaluation seems to miss this point.
NSDI’19 Review: I did not find the corresponding motivation for accelerating intra-host communication in this paper. You might want to show that (1) the performance of intra-host communication is critical for many applications and (2) what performance problems that existing kernel stacks have. The paper does not even show and compare the performance of unix domain sockets or pipes, and simply jumps on improving TCP sockets for intra-host communication.
OSDI’18 Review: Why do you use TCP sockets for intra-machine connections? Why not use a unix domain socket or a pipe? The following page says that using unix domain sockets or pipe() brings 3x better latency and produces 7x better throughput than a TCP connection. …
OSDI’18 Review: Using shared memory for IPC is common. The authors use it for socket communication across processes/threads.

## Slide 10: Linux Socket: from send() to recv()
OS
NIC
Sender Host
Application
Lock
send() syscall
VFS send
Copy data, allocate mem
TCP/IP
TCP send buffer
Network packet
C library
send() socket call
OS
NIC
Receiver Host
Application
Lock
recv() syscall
VFS recv
Copy data, free mem
TCP/IP
TCP recv buffer
Network packet
C library
recv() socket call
Event Notification
Wakeup process
Process Scheduling
Network packet
Packet processing (netfilter, tc…)
Network packet
Packet processing (netfilter, tc…)
Network packet

## Slide 11: Round-Trip Time Breakdown
Type | Overhead (ns) | Linux |  | LibVMA |  | RSocket |  | SocksDirect | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 177 |  | 209 |  | 53 | 
 | C library shim | 12 |  | 10 |  | 10 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A |  | N/A |  | N/A | 
 | Socket FD locking | 160 |  | 121 |  | 138 |  | N/A | 
Per packet | Total | 15000 | 5800 | 2200 | 1300 | 1700 | 1000 | 850 | 150
 | Buffer management | 430 |  | 320 |  | 370 |  | 50 | 
 | TCP/IP protocol | 360 |  | 260 |  | N/A |  | N/A | 
 | Packet processing | 500 | N/A | 130 |  | N/A |  | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 900 | 450 | 900 | 450 | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A |  | N/A |  | N/A | 
 | Process wakeup | 5000 |  | N/A |  | N/A |  | N/A | 
Per kbyte | Total | 365 | 160 | 540 | 381 | 239 | 212 | 173 | 13
 | Copy | 160 |  | 320 |  | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A | 160 | N/A | 160 | N/A
Notes: Categorize into per-operation, per-packet, per-kbyte overheads.
Linux: most overheads in NIC doorbell, DMA, handling NIC interrupt and process wakeup. Other overheads also contribute a large portion of overheads.
LibVMA:

## Slide 12: Takeaways: performance breakdown
SIGCOMM’19 Review: I'd like to see experimental results that don't use the page-remapping technique, plus more details of how this can be managed securely.
SIGCOMM’19 Review: … it fails to highlight how the various pieces to the solution contribute to the performance gains. I would have liked to see the performance gains dissected in more details.
SIGCOMM’19 Review: I would expect that there are some performance vs. compatibility trade-offs here but the paper fails to highlight them and quantify where certain performance gaps existing.
SIGCOMM’19 PC Meeting Summary: There's a lot of engineering work in your solution, but the evaluation doesn't let us separate the relative costs and benefits of the individual choices.

## Slide 13: SocksDirect Design Goals
Compatibility
Drop-in replacement, no application modification
Isolation
Security isolation among containers and applications
Enforce access control policies
High Performance
High throughput
Low latency
Scalable with number of CPU cores
Scalable with number of concurrent connections
Notes: Why remove concurrent connections: When there is a connection,

## Slide 14: Takeaways: remove unnecessary design goals which lead to a complicated design
NSDI’19 Review: Misleading claim. The intro says that the proposed system maintains good performance even with millions of concurrent connections, which sounds very nice. I later find out that this is for supporting millions of connections between TWO processes/threads as they multiplex a single queue for communication. But why is that important? What matters in practice is to support a large number of concurrent connections with millions of remote clients, where you can’t share a queue.
NSDI’19 Review: What is the usage scenario for supporting a million simultaneous connections between two processes over RDMA? The million connections scenario is a web server scenario, which is going to have a (relatively) small number of server processes and a huge number of external clients, and they will be using TCP since it's not internal to a data center.
The real problem in datacenter that SocksDirect did not solve: one storage/DB server with thousands of storage/DB clients, where the traffic is bursty.

## Slide 15: SocksDirect: Fast and Compatible Socket in User Space
Process 1
Process 2
Event queue
Request queue
Application
User Mode
Kernel Mode
Shared Buffer
Event queue
Request queue
Application
Data
Data
Monitor Process
Monitor: user-space daemon process to coordinate global resources and enforce ACL rules.
Processes as a shared-nothing distributed system: use message passing over shared-memory queues.
ACL rules
connect
send
recv
accept

## Slide 16: SocksDirect Supports Different Transports for Data
User App
libsd
User App
libsd
User App
libsd
User App
TCP/IP
TCP/IP
Monitor
Host 1
Host 2
Host 3
No SocksDirect
Monitor
Mem Queue
Mem Queue
Mem Queue
TCP/IP
RDMA
NIC RDMA API
NIC Packet API
NIC RDMA API

## Slide 17: Remove the Overheads (1)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 18: Remove the Overheads (2)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 19: Takeaways: explain application scenario
Example: why need locking?
NSDI’19 Review: It is nice to handle sharing a socket with multiple senders or multiple receivers. However, while required for correct operation, such communication pattern is pretty unusual. Except for a popular scenario that shares a listening socket with multiple processes/threads, I think it would be rare for multiple senders to share a socket to send messages concurrently or the other way around (multiple receivers contend to receive messages simultaneously). If not, please explain which application does this.

## Slide 20: Token-based Socket Sharing
Optimize for common cases.
Be correct for all cases.
Many to one
One to many
Transfer ownership of tokens via monitor.
Socket is shared among threads and forked processes.
Many to one
One to many
Sender 1
Sender 2
Receiver
Queue
Sender
Receiver 1
Receiver 2
Queue
Lock
Lock
Sender 1
Sender 2
Receiver
Queue
Sender
Receiver 1
Receiver 2
Queue
Receive
token
Send
token

## Slide 21: Takeaways: remove unnecessary design goals which lead to a complicated design
OSDI’18 Review: Not sure what’s the benefit of a single queue for all connections of two communicating machines? I think such a design choice makes the implementation unnecessarily complex (e.g., picking from middle of queue). You might want to compare the performance of a single aggregate queue vs. a per-connection queue.
Traditional queue
1 FD = 1 queue
All threads share a queue
Multiplexed queue in previous submissions
N FDs share 1 queue
1 queue per send/recv thread pair

## Slide 22: Handling Fork
Linux semantics requirement:
File descriptors need to be sequential (1,2,3,4,5…).
Sockets are shared for parent and child processes.
Parent process
Child process
FD Table
5 (COW)
FD Table
5 (COW)
Shared pages
FD Table
3
4
SHM (shared)
RDMA QP
3 (on demand)
5
SHM (shared)
SHM Queue
4
SHM (private)
Socket Data
5
Socket Data
3
4
RDMA QP
3
Transport limitations:
RDMA QP cannot be shared among processes.
Socket Data
3
4
5
RDMA QP
3
5

## Slide 23: Takeaways: make trade-offs
OSDI’18 Review: The Linux socket semantics is that "The file descriptor returned by a successful call will be the lowest-numbered file descriptor not currently open for the process." (http://man7.org/linux/man-pages/man2/socket.2.html), which would no longer be true. This change would break (potentially buggy) applications that rely on low-numbered socket descriptors as an index to an array.
In NSDI’19 submission, we found that Redis and Memcached rely on the lowest FD behavior.
NSDI’19 Review: In section 3.2, your system maintains an FD translation table to be compatible with the POSIX standard that returns the lowest unused FD for a new FD. While this maintains the compatibility with existing applications, it incurs a high overhead on a busy server in practice. … Note that other high-performance TCP/IP stacks like MegaPipe and mTCP intentionally avoid this overhead by not conforming to the requirement.
In SIGCOMM’19 submission, we no longer claim socket establishment throughput because it is not important at all in datacenters! (Remove unnecessary design goals)

## Slide 24: Remove the Overheads (3)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 25: Per-socket Ring Buffer
Many sockets share a ring buffer
Receiver segregates packets from the NIC
Buffer allocation overhead
Internal fragmentation
tail
head
tail
head
Traditional ring buffer
SocksDirect per-socket ring buffer
One ring buffer per socket
Sender segregates packets via RDMA or SHM address
Back-to-back packet placement
Minimize buffer mgmt. overhead

## Slide 26: Per-socket Ring Buffer
tail
send_next
head
Sender side
Receiver side
RDMA write data
RDMA write credits (batched)
Two copies of ring buffers on both sender and receiver.
Use one-sided RDMA write to synchronize data from sender to receiver, and return credits (i.e. free buffer size) in batches.
Use RDMA write with immediate verb to ensure ordering and use a shared completion queue to amortize polling overhead.

## Slide 27: Takeaways: refine design according to reviews
NSDI’19 Review: How does SocksDirect recover when the other endpoint fails?
Our approach: two copies of ring buffers on both sender and receiver. (It also enables batching.)

## Slide 28: Remove the Overheads (4)
Type | Overhead | Linux RTT (ns) |  | SocksDirect RTT (ns) | 
 |  | Inter-host | Intra-host | Inter-host | Intra-host
Per operation | Total | 413 |  | 53 | 
 | C library shim | 15 |  | 15 | 
 | Kernel crossing (syscall) | 205 |  | N/A | 
 | Socket FD locking | 160 |  | N/A | 
Per packet | Total | 15000 | 5800 | 850 | 150
 | Buffer management | 430 |  | 50 | 
 | TCP/IP protocol | 360 |  | N/A | 
 | Packet processing | 500 | N/A | N/A | 
 | NIC doorbell and DMA | 2100 | N/A | 600 | N/A
 | NIC processing and wire | 200 | N/A | 200 | N/A
 | Handling NIC interrupt | 4000 | N/A | N/A | 
 | Process wakeup | 5000 |  | N/A | 
Per kbyte | Total | 365 | 160 | 173 | 13
 | Copy | 160 |  | 13 | 
 | Wire transfer | 160 | N/A | 160 | N/A

## Slide 29: Zero Copy via Page Remapping
Problem: page remapping needs syscalls!
Map 1 page: 0.78 us
Copy 1 page: 0.40 us
Solution: batch page remapping for large messages
Map 32 pages: 1.2 us
Copy 32 pages: 13.0 us
Virtual addr
New page
Sender
Send physical page
Data page
Virtual addr
Old page
Receiver

## Slide 30: Summary: Overheads & Techniques
Kernel crossing (syscall) Monitor and library in user space. Shared-nothing, use message passing for communication.
TCP/IP protocol Use hardware-based transports: RDMA / SHM.
Locking of socket FDs Token-based socket sharing. Optimize common cases, prepare for all cases.
Buffer management Per-socket ring buffer.
Payload copy Batch page remapping.
Process wakeup Cooperative context switch.

## Slide 31: Evaluation Setting
User App
libsd
User App
libsd
User App
libsd
Monitor
Host 1
Host 2
Monitor
Mem Queue
Mem Queue
Mem Queue
RDMA
NIC RDMA API
NIC RDMA API
Notes: Use LD_PRELOAD to load libsd library.
Intra-host
Inter-host

## Slide 32: Latency
Intra-host
Inter-host
Notes: Intra-host: 8B latency close to shared memory queue, 4x lower than Rsocket and LibVMA because they use NIC to forward intra-host packets. 35x lower than Linux.
Inter-host: 8B latency even lower than two-sided RDMA send and receive, because we use one-sided RDMA write. Half of Rsocket, performance gain due to buffer management. 7x lower than LibVMA because it needs batching. Latency 17x lower than Linux.

## Slide 33: Throughput
Intra-host
Inter-host
Notes: Intra-host: 8B message throughput 20x of Linux. At 8K it is closest to other systems because we need batching for zero copy, and it is only activated for >=16KB messages. Large messages 13x of Linux.
Inter-host: 8B message throughput 15x of Linux. One socket connection can saturate the 100Gbps link.

## Slide 34: Multi-core Scalability
Intra-host
Inter-host
Notes: Multi-core scalability: SocksDirect almost linearly scalable. Other systems not linearly scalable due to file descriptor locking and packet queue contention. With higher number of cores, the throughput is even worse.
For inter-host, SocksDirect has even higher throughput than bare metal RDMA, because we have batching.

## Slide 35: Takeaways: evaluate not only the best cases
SIGCOMM’19 Review: It also does not help that the evaluation presents results that appear to have been cherry-picked to put SocksDirect in the best scenario.
SIGCOMM’19 Review: I would have liked to see a more thorough evaluation and I would have expected that the paper highlights where SocksDirect is not ideal. Currently my feeling is that these results were chosen as they show the best scenarios.
OSDI’18 Review: Really importantly, what are the edges of your system that don't perform well, or are hard to deploy and maintain? What are the important tradeoffs?

## Slide 36: Application Performance
Nginx HTTP server request latency
Notes: Nginx HTTP server between two hosts: small HTTP messages, 5x lower than Linux. For large message, 13x lower than Linux due to zero copy.

## Slide 37: Takeaways: evaluate with practical applications
NSDI’19 Review: Evaluation setup (in Section 6) is weird. Running a load balancer, web service, and key-value store on the same machine is pretty unconvincing. This seems to emphasize the performance of your intra-host communication, but I don’t think people would provision the services on a single machine.
OSDI’18 Review: What is the experimental setup for the applications in 6.2? What are the load balancer, the web service, and the KV store? Are they located on the same or different machines? If they are on different machines are they communicating using TCP or RDMA?

## Slide 38: Conclusion
Contributions of this work:
An analysis of performance overheads in Linux socket.
Design and implementation of SocksDirect, a high performance user space socket system that is compatible with Linux and preserves isolation among applications.
Techniques to support fork, token-based connection sharing, allocation-free ring buffer and zero copy that may be useful in many scenarios other than sockets.
Evaluations show that SocksDirect can achieve performance that is comparable with RDMA and SHM queue, and significantly speedup existing applications.

## Slide 39: Closing Thoughts
Rejections are common.
Rejections are constructive.
Published papers are not perfect.
Talk with experts both inside and outside your institution.
There is no new thing under the sun. The solution to your (sub-)problem may be already in a paper twenty years ago, or in a paper of another field.
Think why many old, failed techniques are reinvented 30 years later and become successful.

## Slide 40: Thank you! Wish your papers get accepted by the next major conference. Ad: Welcome to Parallel and Distributed Software Lab, Central Software Institute, Huawei 2012 Labs.
Notes: Thank you for listening!